## Slide 1
Technical Assistance on Preparation of River Basin Management Plans for Six Basins EuropeAid/140294/IH/SER/TR
Seppo Hellsten
Jarno Turunen
Hydromorphological assessment in WFD and HMWB in WFD implementation
26.5.2022
6RBMP Hydromorphological Meeting

## Slide 2: Aim of the meeting
Discussion on criteria and scoring system for hydromorphological status assessment proposed by DGWM
Discussion on criteria for HMWBs assessment proposed from DGWM

## Slide 3: Role of hydromorhpology in WFD

## Slide 4: Hydromorphology in WFD

## Slide 5: Natural waterbodies

## Slide 6: Heavily modified and artificial

## Slide 7
Technical Assistance on Preparation of River Basin Management Plans for Six Basins EuropeAid/140294/IH/SER/TR
Heavily modified and artificial waterbodies
Different environmental goals for physically modified waters
Process described in Heavily Modified Water Body (HMWB) & Artificial Water Body (AWB) guidance document (WFD CIS guidance document No. 4

## Slide 8
Yes
HEAVILY MODIFIED
No
Yes
NATURAL
3. Is ecological status good?
No
No
4. Is lowered status based on physical modifications of water bodies?
Yes
5. Is it possible to reach a good ecological status without any significant effects on use of water body (art. 4 (3))?
Yes
NO
6. Is it possible to reach benefits enabled by physical modifications by other means (art. 4 (3))?
2. Is hydromorphological change significant?
1. Is water body artificial?
Yes
ARTIFICIAL
No
Yes
No

## Slide 9
Next slides only optional…

## Slide 10
Yes
HEAVILY MODIFIED
No
Yes
NATURAL
3. Is ecological status good?
No
No
4. Is lowered status based on physical modifications of water bodies?
Yes
5. Is it possible to reach a good ecological status without any significant effects on use of water body (art. 4 (3))?
Yes
NO
6. Is it possible to reach benefits enabled by physical modifications by other means (art. 4 (3))?
2. Is hydromorphological change significant?
1. Is water body artificial?
Yes
ARTIFICIAL
No
Yes
No

## Slide 11: 1. Is waterbody artificial?
Channel build on dry land
Reservoir/Lake which area is more than half on terrestrial land (area has doubled since damming)

## Slide 12
Yes
HEAVILY MODIFIED
No
Yes
NATURAL
3. Is ecological status good?
No
No
4. Is lowered status based on physical modifications of water bodies?
Yes
5. Is it possible to reach a good ecological status without any significant effects on use of water body (art. 4 (3))?
Yes
NO
6. Is it possible to reach benefits enabled by physical modifications by other means (art. 4 (3))?
2. Is hydromorphological change significant?
1. Is water body artificial?
Yes
ARTIFICIAL
No
Yes
No

## Slide 13: 2. Is hydromorphological change significant?
Goal is to distinguish obvious cases
  need of direct hydromorphological criteria
Direct hydromorphological criteria should be waterproof
  change in ecological quality should be significant
  Example of river macroinvertebrates ecological status
Embankment%

## Slide 14
Yes
HEAVILY MODIFIED
No
Yes
NATURAL
3. Is ecological status good?
No
No
4. Is lowered status based on physical modifications of water bodies?
Yes
5. Is it possible to reach a good ecological status without any significant effects on use of water body (art. 4 (3))?
Yes
NO
6. Is it possible to reach benefits enabled by physical modifications by other means (art. 4 (3))?
2. Is hydromorphological change significant?
1. Is water body artificial?
Yes
ARTIFICIAL
No
Yes
No

## Slide 15: 3. Is ecological status good?
When ecological status is good, water body cannot be designated as heavily modified, although hydro-morphological change is significant
Difficult task for defining ecological status
  Temporary/seasonal waters
  Ecological indicators are sensitive for eutrophication, not hydromorphological change
  Ecological data is missing

## Slide 16
Yes
HEAVILY MODIFIED
No
Yes
NATURAL
3. Is ecological status good?
No
No
4. Is lowered status based on physical modifications of water bodies?
Yes
5. Is it possible to reach a good ecological status without any significant effects on use of water body (art. 4 (3))?
Yes
NO
6. Is it possible to reach benefits enabled by physical modifications by other means (art. 4 (3))?
2. Is hydromorphological change significant?
1. Is water body artificial?
Yes
ARTIFICIAL
No
Yes
No

## Slide 17: 4. Is lowered status based on physical modifications of water bodies?
Easy
  large lakes, dammed rivers
Difficult
  eutrophicated small rivers
  shallow regulated lakes
  lakes with lowered water level

## Slide 18: Impacts of lake water level regulation Lake Oulujärvi
M.Marttunen, S.Hellsten and A.Keto 2001:
Sustainable development of Lake regulation in Finnish lakes.
Vatten 57:29-37. Lund 2001
Natural
Regulated

## Slide 19
Winter draw-down summarises the environmental effects of water level regulation!

## Slide 21
Yes
HEAVILY MODIFIED
No
Yes
NATURAL
3. Is ecological status good?
No
No
4. Is lowered status based on physical modifications of water bodies?
Yes
5. Is it possible to reach a good ecological status without any significant effects on use of water body (art. 4 (3))?
Yes
NO
6. Is it possible to reach benefits enabled by physical modifications by other means (art. 4 (3))?
2. Is hydromorphological change significant?
1. Is water body artificial?
Yes
ARTIFICIAL
No
Yes
No

## Slide 22: 5. Is it possible to reach a good ecological status without any significant effects on use of water body (art. 4 (3))?
Physical modifications are due to flood protection, hydropower production, irrigation, drinking water need and recreational use.
Problematic term ”significant effect on use”
  local, regional or national significance?
Value of water should be evaluated
Wikipedia

## Slide 23
Yes
HEAVILY MODIFIED
No
Yes
NATURAL
3. Is ecological status good?
No
No
4. Is lowered status based on physical modifications of water bodies?
Yes
5. Is it possible to reach a good ecological status without any significant effects on use of water body (art. 4 (3))?
Yes
NO
6. Is it possible to reach benefits enabled by physical modifications by other means (art. 4 (3))?
2. Is hydromorphological change significant?
1. Is water body artificial?
Yes
ARTIFICIAL
No
Yes
No

## Slide 24: 6. Is it possible to reach benefits enabled by physical modifications by other means (art. 4 (3))?
Usually easy to analyse
  Hydropower lakes alternative means for hydropower production are more harmful for environment – wind or solar power?
  Other options for flood protection and irrigation are difficult
There might be some obsolate dams is small rivers
  Dam removal processes taking place all over Europe
Tuulivoimayhdistys

## Slide 25
Yes
HEAVILY MODIFIED
No
Yes
NATURAL
3. Is ecological status good?
No
No
4. Is lowered status based on physical modifications of water bodies?
Yes
5. Is it possible to reach a good ecological status without any significant effects on use of water body (art. 4 (3))?
Yes
NO
6. Is it possible to reach benefits enabled by physical modifications by other means (art. 4 (3))?
2. Is hydromorphological change significant?
1. Is water body artificial?
Yes
ARTIFICIAL
No
Yes
No

## Slide 30: Defing hydromorphological status in coastal waters
Share of constructed shoreline of total shoreline (%)
Share of modified/dredged bottom (%)
Effect of bridges and embankments (%)
Natural connection to open sea
 | Share of constructed shoreline of total shoreline (%) | Share of modified/dredged bottom (%) | Effect of bridges and embankments (%) | Natural connection to open sea
Very high (4 points) | > 50 | >5 | Case specific evaluation | Completely closed
High (3 points) | 20-50 | >2-5 | Case specific evaluation | Mostly closed
Moderate (2 points) | 10-20 | 1-2 | Case specific evaluation | Partly closed
Slight (1 points) | <10 | <1 | Case specific evaluation | Partly affected
No change (O points) | <5 | 0 | Case specific evaluation | Open

## Slide 31
Level of hydro-morphological change | Changes in the hydro-morphological status | HyMo-points
0 | No change | 0 – 1
1 | Slight change | 2 – 3
2 | Quite significant change | 4 – 5
3 | Significant change | 6 – 9
4 | Very significant change | 10 ->
HyMo-points
0-1 p.
2-3 p.
4-5 p.
6-9 p.
10- p.
Excellent status
Moderate status or
worse
Heavily modified
Evaluation of hydromorphological change by Hymo-criteria – total scoring

## Slide 32
Discussion on criteria and scoring system for hydromorphological status assessment proposed by DGWM

## Slide 33: River HyMo-status assessment parameters
Hydromorphological Monitoring and Assessment Parameters​
1. Longitudinal Flood Structures​
2. Transitional Structures​
3. Regulators​
4. The Effects of Dams and Ponds in the Drainage Area​
5. The Effect of Flow Variation Caused by Hydroelectric Power Plants​
6. Structures That Do Not Allow Sediment Transition​
7. Structures That Do Not Allow Fish Passage​
8. Unnatural Land Use (30m)​
9. Unnatural Land Use (100m)​
10. Natural Vegetation (30m)​
11. Natural Vegetation (100m)​
12. Water Abstraction​
Alltogether 12 parameters
All are very suitable to WFD requirements
However, less detail could be enough for the
requirements of WFD?
Intercorrelation between the parameters? No
loss of key HyMo-information with less variables?
Possible to do lighter hymo assessment for the
present project needs?
WFD

## Slide 34: River HyMo-parameter suggestions to WFD assessment in 6Basins
1. Longitudinal flood structures
  Excellent parameter to describe connecitivity to
  floodplains and channelization
4. The Effects of Dams and Ponds in the Drainage Area
  Excellent parameter to describe ecological connectivity
7. Structures That Do Not Allow Fish Passage​
  Excellent parameter to describe ecological connectivity
  Might also capture changes in sediment transition
10. Natural Vegetation (30m)​
  Riparian land use important variable in WFD hymo-asses
  sment
  One land use parameter should be enough, 30 m scale is
  probably more ecologically influential than 100 m scale
12. Water Abstraction​
  Important parameter to quantify deviations from natural flow regime

## Slide 35: Lakes HyMo-status assessment parameters
Hydromorphological Monitoring and Assessment Parameters​
1. Lake Surface Area Change​
2. The Effect of Dams and Ponds of which Reservoir is Located in the Drainage Area on the Hydrological Regime of the Lake​
3. Regulator​
4. Transitional Structures​
5. Longitudinal Flood Structures;​
6. Lake Coast Embankment and Modification Status on the Coast​
7. Unnatural Land Use (30m)​
8. Unnatural Land Use (100m)​
9. Natural Vegetation (30m)​
10. Natural Vegetation (100m)​
11. Water Abstraction​
Alltogether 11 parameters
All are very suitable to WFD requirements
However, less detail could be enough for the
requirements of WFD?
Intercorrelation between the parameters? No
loss of key HyMo-information with less variables?
Possible to do lighter hymo assessment for the
present project needs?
WFD

## Slide 36: Lake HyMo-parameter suggestions to WFD assessment in 6basins
1. Lake Surface Area Change
  Excellent parameter to quantify morphological changes
3. Regulator
  Important to quantify water flow regulators that influence lake inflow
6. ​Lake Coast Embankment and Modification Status on the Coast​
  Excellent parameter to assess lake shore naturalness
11. Water abstraction
  Important variable to quantify water level fluctuation
Riparian land use has less importance in lakes compared to streams

## Slide 37: Transitional river HyMo-status assessment parameters
Hydromorphological Monitoring and Assessment Parameters​
1. Longitudinal Flood Structures​
2. Transitional Structures​
3. Regulators​
4. The Effects of Dams and Ponds in the Drainage Area​
5. The Effect of Flow Variation Caused by Hydroelectric Power Plants​
6. Structures That Do Not Allow Sediment Transition​
7. Structures That Do Not Allow Fish Passage​
8. Unnatural Land Use (30m)​
9. Unnatural Land Use (100m)​
10. Natural Vegetation (30m)​
11. Natural Vegetation (100m)​
12. Water Abstraction​
13. Structures That Affect the Wave Flow​
Alltogether 13 parameters
All are very suitable to WFD requirements
However, less detail could be enough for the
requirements of WFD?
Intercorrelation between the parameters? No
loss of key HyMo-information with less variables?
Possible to do lighter hymo assessment for the
present project needs?
WFD

## Slide 38: Transitional river HyMo-parameter suggestions to WFD assessment in 6basins
1. Longitudinal flood structures
  Excellent parameter to describe connecitivity to
  floodplains and channelization
4. The Effects of Dams and Ponds in the Drainage Area
  Excellent parameter to describe ecological connectivity to upstream
  form the transitional area
5. The Effect of Flow Variation Caused by Hydroelectric Power Plants​
  Flow variation due to hydropower production can have a large effect
  on the salinity of the transitional zone
7. Structures That Do Not Allow Fish Passage
  Excellent parameter to describe ecological connectivity
  Might also capture changes in sediment transition
12. Water Abstraction​
  Important parameter to quantify deviations from natural flow regime→
  influences the salinity gradient
13. Structures That Affect the Wave Flow​
  Good parameter to describe changes in wave and tidal influence

## Slide 39: Transitional lakes HyMo-status assessment parameters
Hydromorphological Monitoring and Assessment Parameters​
1. Lake Surface Area Change​
2. The Effect of Dams and Ponds of which Reservoir is Located in the Drainage Area of the Lake on the Hydrological Regime of the Lake​
3. Regulator​
4. Transitional Structures​
5. Longitudinal Flood Structures;​
6. Lake Coast Embankment and Modification Status on the Coast​
7. Unnatural Land Use (30m)​
8. Unnatural Land Use (100m)​
9. Natural Vegetation (30m)​
10. Natural Vegetation (100m)​
11. Water Abstraction​
12. Structures That Affect the Wave Flow​
Alltogether 12 parameters
All are very suitable to WFD requirements
However, less detail could be enough for the
requirements of WFD?
Intercorrelation between the parameters? No
loss of key HyMo-information with less variables?
Possible to do lighter hymo assessment for the
present project needs?
WFD

## Slide 40: Transitional lake HyMo-parameter suggestions to WFD assessment in 6basins
1- Lake Surface area reflects change in volume.
2. The Effect of Dams and Ponds of which Reservoir is Located in the Drainage Area of the Lake on the Hydrological Regime of the Lake​
  Good parameter to quantify changes in freshwater inflow to transitional lake lagoon
11. Water abstraction
  Good parameter to quantify water withdrawal affecting flow regime to transitional lake lagoon
12. Structures that affect wave flow
  Good parameter to quantify changes in wave exposure and tidal influence
Hydromorphological Monitoring and Assessment Parameters​
1. Lake Surface Area Change​
2. The Effect of Dams and Ponds of which Reservoir is Located in the Drainage Area of the Lake on the Hydrological Regime of the Lake​
3. Regulator​
4. Transitional Structures​
5. Longitudinal Flood Structures;​
6. Lake Coast Embankment and Modification Status on the Coast​
7. Unnatural Land Use (30m)​
8. Unnatural Land Use (100m)​
9. Natural Vegetation (30m)​
10. Natural Vegetation (100m)​
11. Water Abstraction​
12. Structures That Affect the Wave Flow​

## Slide 41: Coastal HyMo-status assessment parameters and WFD suggestions
Hydromorphological Monitoring and Assessment Parameters​
1. Coastal Length with Anthropogenic Structures.​
2. Land Use in the Area Near the Coast​
3. The Effect of Large Barriers in the Drainage Area on the Flow Regime​
4. Structures that Affect the Wave Regime​
Alltogether 4 parameters
2 parameters could be enough for WFD requirements
1. Coastal Length with Anthropogenic Structures.​
  Good parameter to quantify coastal infrastructure
  and modifications.
4. Structures that affect the wave regime
  Good parameter to quantify changes in wave exposure
WFD

## Slide 42
Discussion on criteria for HMWBs assessment proposed from DGWM

## Slide 43: Defining Environmental objectives

## Slide 45
Setting environmental objectives!

## Slide 46: Examples of restoration measures in rivers
Reduction of water level fluctuation
Enhancing river continuity by fish ways and bypass channels
Restoration of main channel and shores
Restoration of bypass channels
Restoration of tributaries
Removal of old protecting structures and modification of littoral areas

## Slide 47
How much we can harm use of water body to reach GOOD ecological potential!
  Estimations between 0,5 – 3 % of hydropower price etc.
THE MOST DIFFICULT ISSUES
There is no sense to build fishway, if there are no spawning grounds available
  How much stocking is allowed
Restoration costs are part of programme of measures
  Skip them in designation and ecological status assessment

## Slide 48: Proposal of AWB/HMWB designation

## Slide 49: Rivers – HMWB/AWB designation suggestions in 6basins
Dams and Ponds > 50%
Water Abstraction or Water Transfer > 50%
Irrigation and HEPP Regulators > 2 per km
Coastal Reinforcement or Coastal Flood Structures > 60%

## Slide 50: Lakes – HMWB/AWB designation suggestions in 6basins
The Amount of Change in the Lake Surface Area > 40%
Coastal Reinforcement or Coastal Flood Structures > 60%

## Slide 51: Transitional rivers – HMWB/AWB designation suggestions in 6basins
Dams and Ponds
  (Dam Inlet Flow - Dam Outlet Flow) / Dam Inlet Flow ratio >30%
Coastal Reinforcement or Coastal Flood Structures >50%

## Slide 52: Transitional lakes – HMWB/AWB designation suggestions in 6basins
The Amount of Change in the Lake Surface Area > 40%
Structures which affect on wave and tidal flow?

## Slide 53: Coastal waters – HMWB/AWB designation suggestions in 6basins
Anthropogenic Structures in the Coastal Water Body > 40%

## Slide 54
Thank you for your attention!
Seppo.Hellsten@syke.fi
Jarno.Turunen@syke.fi